## Slide 1
Network Architecture: GCP Dedicated Interconnect
Voice & Data Private Connectivity for Contact Center AI
Dual DC (Dallas + Phoenix) | 99.99% SLA | < 80ms Voice Latency
Five9 IVR | GCP CCAI | Genesys Cloud Agent Desktop

## Slide 2
Network Topology Overview
Dallas DC (Primary)
Phoenix DC (DR)
Equinix DA7
Equinix DA2
Equinix PH1
GCP us-south1 (Dallas)
GCP us-central1 (Iowa/DR)
Five9 Cloud IVR
Genesys Cloud CX
10G
10G Dedicated
Legend:
Voice Path (SIP/RTP)
Data Path (HTTPS)
• Dallas DC & Phoenix DC connect to Equinix meet-me rooms • 10 Gbps Dedicated Interconnect to GCP regions • Five9 IVR connects via GCP backbone • Genesys receives calls post-AI processing

## Slide 3
GCP Region Selection
PRIMARY: us-south1 (Dallas)
• Latency: < 2ms (same metro as Dallas DC) • Role: Primary CCAI processing • Interconnect: DA7 + DA2 (dual path) • Services: Dialogflow CX, Cloud Run, Speech-to-Text, Text-to-Speech, Firestore
DR: us-central1 (Iowa)
• Latency: 15-20ms from Phoenix DC • Role: Disaster Recovery • Interconnect: PH1 + PHX1 (dual path) • Services: Full CCAI stack (replicated) • Activation: < 30 second failover
Key GCP Services Available in Both Regions:
Dialogflow CX
Cloud Run
Speech-to-Text
Text-to-Speech
Firestore
BigQuery

## Slide 4
Dedicated Interconnect: 99.99% Redundancy
DA7 (AT&T) Dallas Metro
── 10 Gbps ── VLAN 100 (Voice) + VLAN 200 (Data) ──▶
GCP us-south1
Primary Path A
DA2 (Verizon) Dallas Metro
── 10 Gbps ── VLAN 100 (Voice) + VLAN 200 (Data) ──▶
GCP us-south1
Primary Path B
PH1 (AT&T) Phoenix Metro
── 10 Gbps ── VLAN 100 (Voice) + VLAN 200 (Data) ──▶
GCP us-central1
DR Path A
PHX1 (Verizon) Phoenix Metro
── 10 Gbps ── VLAN 100 (Voice) + VLAN 200 (Data) ──▶
GCP us-central1
DR Path B
BGP: Customer ASN 64512 ↔ Google ASN 16550 | BFD Enabled (failover < 5 seconds) | MED-based primary/backup routing

## Slide 5
Voice Path: On-Prem SBC → GCP CCAI → Genesys Agent
PSTN Inbound
Oracle SBC
Dedicated Interconnect
GCP GTP/LB
Dialogflow CX (CCAI)
Return via Interconnect
Genesys Agent
→
→
→
→
→
→
Key Voice Path Specifications: • Protocol: SIP over TLS (Port 5061) • Media: SRTP (encrypted RTP) • Codec: G.711 μ-law (64 kbps) • Target Latency: < 80ms one-way • QoS: DSCP EF (46) for voice packets • Capacity: 500 concurrent sessions per SBC pair
Voice Quality Requirements
• MOS Score: > 4.0 target • Jitter: < 30ms • Packet Loss: < 1% • One-way Delay: < 80ms • Echo Cancellation: Enabled on SBC

## Slide 6
Data Path: Genesys ORS → GCP Middleware (Private)
Genesys ORS
Interconnect (data-vlan)
Private Service Connect
Cloud Run Middleware
Firestore / BigQuery
──▶
──▶
──▶
──▶
Key Data Path Characteristics: • No Public IP addresses - fully private • Private Service Connect endpoint for GCP services • mTLS authentication between services • Target latency: < 50ms round-trip • VLAN 200 (data) separated from voice traffic • Cloud Armor WAF for API protection
Data Integration Patterns
• Screen Pop: ORS → Cloud Run → Agent Desktop (Customer context in < 200ms) • Post-Call: Recording → GCS → BigQuery (Analytics pipeline) • Real-time: CCAI hints → Genesys routing (Intent-based call routing)

## Slide 7
GCP VPC Design & VPC Service Controls
VPC Service Controls Perimeter
VPC: ccai-prod-vpc
voice-subnet 10.100.0.0/24
data-subnet 10.101.0.0/24
ccai-subnet 10.102.0.0/24
• SBC Landing • Voice GW • RTP Processing
• Cloud Run • API Gateway • PSC Endpoints
• Dialogflow CX • STT/TTS • Firestore
Firewall: Deny-all default | Allow voice: TCP 5061, UDP 16384-32767 | Allow data: TCP 443 only
Security Controls
✓ Private Google Access ✓ No Public IP addresses ✓ VPC Service Controls ✓ Cloud Armor WAF ✓ mTLS service mesh ✓ CMEK encryption ✓ Cloud Audit Logs ✓ DLP API integration

## Slide 8
Latency Budget: Voice Path (< 80ms Target)
Segment
Latency
Visual Budget
DC → Equinix
< 1ms
Equinix → GCP Edge
1-2ms
GCP Internal Routing
1-2ms
CCAI Processing
50-100ms
Return Path (GCP → DC)
3-5ms
TOTAL (Typical)
60-80ms
✓ WITHIN TARGET
Notes: • CCAI processing is the dominant factor (50-100ms depending on complexity) • Network transport adds only 5-10ms total (benefit of Dedicated Interconnect) • Worst case with DR failover to us-central1: adds 15-20ms (still within 150ms budget)

## Slide 9
High Availability & Disaster Recovery
Layer 1: SBC HA
< 3 seconds
Active/Standby SBC pair Automatic session preservation
Layer 2: Interconnect
< 5 seconds
4x 10G links (2 per metro) BFD detection + BGP re-route
Layer 3: Geographic DR
< 30 seconds
Dallas → Phoenix failover DNS + BGP path change
Layer 4: GCP Region
< 30 seconds
us-south1 → us-central1 Cross-region load balancing
Combined SLA: 99.99%
Zero single points of failure: Dual DC | Dual ISP | Dual GCP Region | Dual SBC

## Slide 10
Investment & Implementation Timeline
Monthly Recurring Cost
Dedicated Interconnect (4x 10G)
$10,953
GCP Services (CCAI, Compute, Storage)
$4,625
Total Monthly: ~$15,578/month
Implementation Timeline: 12 Weeks
Phase 1: Procurement
Wk 1-4
Cross-connects, LOAs, ISP circuits
Phase 2: GCP Infra
Wk 3-6
VPC, interconnect attach, Cloud Router
Phase 3: Security
Wk 5-7
VPC-SC, firewall rules, mTLS, testing
Phase 4: Go-Live
Wk 9-12
Integration test, cutover, monitoring
Wk1 Wk2 Wk3 Wk4 Wk5 Wk6 Wk7 Wk8 Wk9 Wk10 Wk11 Wk12