## Slide 1
Five9 IVR + Genesys Agent Bridge
Voice & Data Bridge Architecture for CCaaS Migration
Executive Presentation | Migration Architecture
Five9
+
Genesys

## Slide 2
Agenda
1
Executive Summary & Business Context
2
Solution Architecture Overview
3
End-to-End Call Flow
4
Component Architecture (Five9 / SBC / Genesys / GCP)
5
Data Conservation & Unified Correlation
6
Failover & Resilience Strategy
7
Monitoring & Observability
8
Deployment Approach & Timeline
9
Risks & Mitigations

## Slide 3
Executive Summary
The Challenge
Migrate from on-premises Genesys Engage to Five9 CCaaS while maintaining uninterrupted service. During migration, Five9 handles IVR while all agents remain on Genesys. Call context must be preserved across both platforms.
The Solution
Five9 IVR handles all inbound calls (menu routing)
Oracle SBC bridges SIP between Five9 and Genesys
GCP Cloud Run middleware preserves call context
Genesys agents receive calls with full IVR data
Unified correlation ID tracks calls across platforms
Bidirectional transfer support (Five9 <-> Genesys)
Key Parameters
Volume
10,000 calls/day
Architecture
Temporary (migration)
Five9 Role
IVR front-end only
Genesys Role
All agent interactions
SBC
Oracle/Acme Packet (Dual HA)
Media Path
Five9 stays in path
ANI
Original caller preserved
Failover
Callback / queue on Five9
Data
Full bidirectional context
Reporting
Unified via BigQuery

## Slide 4
Solution Architecture Overview
Caller (PSTN)
-->
Oracle SBC (Dual HA) HMR Routing Media Anchor
-->
Five9 Cloud IVR Menu Routing Self-Service Recording
<--
-->
Genesys Engage (On-Prem) SIP Server (HA) ORS/URS Agent Groups Skills Routing Workspace Desktop
GCP Cloud Run Middleware Context Store CRM Enrichment Correlation
GCP Analytics Firestore Pub/Sub BigQuery
-->
-->
Legend:
Five9 (IVR)
Genesys (Agents)
Oracle SBC
GCP Services
Key Design Decisions
* Five9 stays in media path * SBC anchors all RTP * ANI preserved end-to-end * Graceful failover to Five9 * Unified correlation ID

## Slide 5
End-to-End Call Flow
1 Caller dials (PSTN)
->
2 SBC routes to Five9
->
3 Five9 IVR (Menu)
->
4 Webhook to GCP API
->
5 SIP Transfer + X-Headers
->
6 SBC HMR (Normalize)
->
7 Genesys ORS (Route)
->
8 Agent (Screen Pop)
Data Conserved at Each Step:
Step 3 (Five9 IVR)
ANI, DNIS, Language, Menu Choice, Intent, Priority, CustomerID, Account Balance
Step 4 (GCP Webhook)
All IVR data + Five9 UUID + Correlation ID -> stored in Firestore (enriched with CRM data)
Step 5 (SIP Transfer)
12 X-Headers carrying all context + P-Asserted-Identity (original ANI)
Step 6 (SBC HMR)
Headers normalized: X-Five9-* -> X-Bridge-* format for Genesys consumption
Step 7 (Genesys ORS)
Headers mapped to UserData KVPs + middleware API call for full enriched context
Step 8 (Agent)
Full screen pop: Customer Name, Intent, Balance, IVR Path, Correlation ID, Priority

## Slide 6
SIP Transfer: Voice + Data Bridge
SIP INVITE (Five9 -> SBC -> Genesys)
INVITE sip:RP_Billing@sbc-a.company.com SIP/2.0 P-Asserted-Identity: <sip:+15551234567@company.com> X-Five9-CorrelationId: 550e8400-e29b-41d4... X-Five9-Intent: billing X-Five9-CustID: CUST-99001 X-Five9-Language: en X-Five9-MenuChoice: 1 X-Five9-Priority: normal X-Five9-CallUUID: five9-sess-abc123 X-Five9-ANI: +15551234567 X-Five9-DNIS: 18005551234 X-Five9-Balance: $1,234.56 X-Five9-Timestamp: 2024-03-15T10:30:00Z Content-Type: application/sdp m=audio 20000 RTP/AVP 0 8 101 (G.711u/a)
SBC Header Manipulation (HMR)
1. Maps X-Five9-* headers -> X-Bridge-* format 2. Preserves original ANI in P-Asserted-Identity 3. Strips Five9-specific topology info 4. Rewrites Request-URI to Genesys RP address 5. Anchors media (RTP stays through SBC) 6. Applies TLS termination (Five9=TLS, Genesys=TCP)
Genesys SIP Server Processing
1. Receives INVITE on Trunk DN (TRK_Five9_Bridge_In) 2. Extracts X-Bridge-* headers -> UserData KVPs 3. Routes to RP_Bridge_Entry (master routing point) 4. ORS strategy reads UserData + calls GCP API 5. Routes to AG_Billing with priority & language skills 6. Agent receives call + full Five9 IVR context screen pop

## Slide 7
Data Conservation: Unified Correlation
Single Correlation UUID travels across all 4 platforms:
Five9 CAV + Call Log + Recording
->
Oracle SBC CDR + SIP Trace Logs
->
GCP Firestore Doc ID + BigQuery + Pub/Sub
->
Genesys UserData + Info Mart + Pulse + Recording
Correlation ID: 550e8400-e29b-41d4-a716-446655440000
Data Fields Conserved End-to-End (12 fields in SIP + enriched via API):
ANI (original caller)
DNIS (number dialed)
Language (en/es)
Menu Choice (1-5)
Intent (billing/sales/tech)
Customer ID
Account Balance
Priority (high/normal)
Five9 Call UUID
IVR Timestamp
IVR Duration
Transfer Target (RP name)
+ CRM-enriched fields from GCP middleware: Customer Name, Segment (VIP/Standard), Account Type, Open Cases, Last Interaction Date

## Slide 8
Failover & Resilience Strategy
Genesys Down
SBC OPTIONS ping detects failure Returns 503 to Five9
Five9 offers callback or queues caller
SBC Failure
HA heartbeat miss (500ms) Standby SBC takes over
1-2 second blip Active calls preserved
GCP Middleware Down
ORS HTTP timeout (5s) Graceful degradation
Routes with SIP headers only No enriched data but call works
Five9 Platform Outage
SBC detects Five9 OOS via OPTIONS ping
SBC routes PSTN directly to Genesys (bypass Five9)
Failure
Detection
Caller Experience
Design Principle: No single component failure drops a call. Caller always gets callback option or stays in queue.

## Slide 9
Monitoring & Unified Observability
Key Performance Indicators
Transfer Success Rate
> 99%
SBC CDR
Transfer Latency (p95)
< 15 sec
Middleware timestamps
Middleware API Latency
< 500ms
Cloud Run metrics
Correlation Match Rate
> 98%
Firestore vs Genesys
SBC Capacity Used
< 80%
SNMP polling
Monitoring Stack
GCP Cloud Monitoring
Dashboards, alerting, uptime checks
Cloud Logging
Structured logs with correlation ID
BigQuery
Unified cross-platform reporting
Pub/Sub
Real-time event streaming for NOC
PagerDuty/Slack
P1 alerts for transfer failures
Critical Alert Rules
Transfer failure > 5% (5 min) -> P1
Middleware p99 > 3s -> Warning
Genesys SIP unreachable -> P1
SBC capacity > 90% -> Warning
Correlation miss > 10% -> P2

## Slide 10
Deployment Approach & Timeline
Phase 1 Infra Setup
Week 1-2
SBC deploy, GCP infra, TLS certs, connectivity
->
Phase 2 Config
Week 3-4
Five9 IVR, Genesys objects, SBC HMR, middleware API
->
Phase 3 Testing
Week 5-6
E2E calls, failover tests, load test (50 concurrent)
->
Phase 4 Pilot
Week 7-8
10% traffic, monitor 48h, ramp to 50%, then 100%
Go-Live Success Criteria:
99%+ transfer success rate over 48-hour pilot window
All SIP headers correctly passing through (verified via SIP traces)
Agent screen pop displays full Five9 IVR context on every call
Failover tested: Genesys down -> caller gets callback within 30s
Unified correlation ID visible in both Five9 reports AND Genesys Info Mart

## Slide 11
Risks & Mitigations
Risk
Impact
Mitigation
Level
SIP Header Interop
Five9 may lowercase/modify headers
SBC HMR normalizes; tested in lab
Medium
Voice Quality
Additional SBC hop adds latency
G.711 codec; < 5ms added per hop
Low
Genesys Dependency
Agents unavailable = callers stuck
Five9 offers callback within 30s
Medium
Middleware Latency
GCP API adds to call setup time
Graceful degradation; routes without enrichment
Low
Data Loss on Failure
Context not reaching Genesys
Dual path: SIP headers + HTTP API (belt & suspenders)
Low
Migration Rollback
Need to revert to direct Genesys IVR
SBC policy change (1 CLI command) reverts traffic
Low

## Slide 12
Recommended Next Steps
1. Approve architecture and proceed with Phase 1 (Infrastructure Setup)
2. Engage Five9 TAM for SIP trunk provisioning and custom header enablement
3. Provision Oracle SBC lab environment for SIP interop testing
4. Stand up GCP project and deploy Cloud Run middleware (dev/staging)
5. Schedule Genesys Configuration Server change window (Trunk DN + ORS deploy)
6. Define pilot DNIS list (10% of traffic) and success criteria sign-off
7. Establish monitoring dashboards and PagerDuty escalation paths
Target: Production Go-Live in 8 weeks